System Test Engineer

---
What is a Car?
What is a Car?
A car (or automobile) is a wheeled motor vehicle used for transportation.

---
Functionalities of a car
Functionalities of a car

---
What is an ECU?
What is an ECU?
An electronic control unit (ECU) is any embedded system in automotive electronics that controls one or more of the electrical systems or subsystems in a vehicle.

---
What is an ECU?
What is an ECU?
An electronic control unit (ECU) is any embedded system in automotive electronics that controls one or more of the electrical systems or subsystems in a vehicle.

---
Types of ECU
Types of ECU
- Door Control Unit
- Engine Control Unit
- Brake Control Unit
- Airbag Control Unit
- Battery Management System etc

---
Network Protocols
Network Protocols
CAN
- LIN
- MOST
UDS
- CAN FD
- FlexRay
- Automotive Ethernet

---
IN-Vehicle Architecture
IN-Vehicle Architecture

---
V Model- Software Development Lifecycle of an ECU
V Model- Software Development Lifecycle of an ECU
Course Focus

---
Need for Network Arbitration
Need for Network Arbitration
- A mordern car has around 70 ECUs
- Some of the ECUs work independently, but all other need communications to be established between them
- CAN is used to achieve this communication

---
CAN
CAN
CAN is a multi-master serial bus standard for connecting Electronic Control Units (ECUs) also known as nodes.
Two or more nodes are required on the CAN network to communicate.
The complexity of the node can range from a simple I/O device up to an embedded computer with a CAN interface and sophisticated software.
All nodes are connected to each other through a two wire bus. The wires are a twisted pair with a 120 Ω (nominal) characteristic impedance.

---
CAN BUS
CAN BUS
CAN H
CAN BUS
CAN L
CAN
NODE 1
CAN
NODE 3
CAN
NODE 2

---
Mesh
2
1
4
3

---
CAN Frame Format
CAN Frame Format

---
CAN Message frame
CAN Message frame

---
CAN HIGH and LOW
CAN HIGH and LOW
‘0’ is represented by (3.75V - 1.25V) = 2.5V
‘1’ is represented by = 0V

---
CAN
CAN
CAN Properties:
The bus can have one of two complimentary logical:
Dominant ‘0’
Recessive ‘1’
During the simultaneous transmission of ‘dominant’ and ‘recessive’
bits the resulting bus value will be ‘dominant’
CAN is a broadcast message protocol

---
CAN
CAN
- BRAKE ECU ID ‘0101’
- Window Panel ECU ID ‘1011’
- If both the ECUs start transmitting simultaneously in the CAN bus then the BRAKE ECU will be selected. The window panel ECU will wait and retransmit.
- This provides prioritisation and avoids collision

---
CAN H
CAN BUS
0010
CAN L
0101
1011
0010
CAN
Seat belt
ECU
CAN
Accelerator
CAN
Brake
CONTI
BOSCH
X

---
Types of CAN FRAMES
Types of CAN FRAMES
Data Frame
  - 99% of transmission
- Remote Frame
- Error Frame
  - Every device/node calculates the CRC
  - If any device finds a mistake; the EOF will be turned ‘dominant’.
  - Every other device will throw the frame

---
Youtube link to install Linux
Youtube link to install Linux
https://youtu.be/DC89AryJEE8

---
DAY 2
- Initiatlizing Socket CAN
- Sending and Receiving messages on Socket CAN
- Number Systems
- ECLIPSE INTRO
- Python Intro
- Strings
- Integers

---
VCan/Socket CAN
VCan/Socket CAN
Is a set of open source CAN drivers & a networking stack.
Traditional CAN drivers allowed only allow sending to and receiving from the CAN controller. Supported only a single process at a time. All other processes-blocked.
The Socket CAN allows multiple applications to access one CAN device simultaneously.
Also, a single application is able to access multiple CAN networks in parallel.
Communication with the CAN bus is done analogously to the use of the Internet Protocol via sockets.

---
CAN H
VCAN0
CAN L
0010
CAN
BRAKE
CAN
CRASH
CAN
Window
Sensor
Motor

---
VCan/Socket CAN
``shell
pip3 install python-can
pip3 install cantools
pip3 install can-isotp
pip3 install canmatrix
    sudo modprobe vcan	# setup vcan
    sudo ip link add vcan0 type vcan	# setp vcan0 as vcan
    sudo ip link set up vcan0	#initializes the vcan0
    cansend vcan0 001#1234567890AABBCC
    Candump any # puts receiver in listening mode
    cangen vcan0	# sends periodic
    candump -help	# for further help in can

---
Number Types_clipboard0
Number Types
Binary, Decimal, Hexa
Binary – Base2 (0 ,1)
Decimal – Base10 (0,1,2,3,4,5,6,7,8,9)
Hexa - Base 16 (0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F)
We All understand DECIMAL. Number 231 is a decimal.
231 in binary ( 0 1 2 3 4 5 6 7 8 9)
231=128+64+32+4+2+1= 224
        28 27 26 25 24 23 22 21 20
        256 128 64 32 16 8 4 2 1
        1 1 1 0 0 1 1 1
Binary 0 1

---
Number Types
Number Types
HEXA —0 1 2 3 4 5 6 7 8 9 A B C D E F
c. 231 in hexa
        168 167 166 165 164 163 162 161 160
        256 16 1
        E 7
14x16 =224+
7x1 = 7
        = 231

---
Number Types_clipboard1
Number Types
Why do you have a 4 bit identifier
123#12 34 FF AA BB
THE COMPUTER WILL READ THE DATA AS
123# 0100100 00110100 11111111 10101010 10111011

---
Python Key words
and	else
except	break
False	class
True	continue
for	def
from	del
Global	if
import	elif
in	or
Lambda	while

---
CAN H
VCAN0
CAN L
001x 1234
CAN
CRASH
ON EVENT
CAN
SEAT Belt
ECU
CAN
Airbag
CRASH Sensor
ON EVENT
KEYBOARD
Motor

---
ECU Task- CAN
Send and Receive CAN Messages
ACTION- ON EVENT (crash detected value comes from sensor)- key press
ACTION- ON MESSAGE (value comes from other ECUs)

---
 ECU – development team
DBC file and the requirement
Develop the ECU
Written a python code for ECU development
System testing Team
If this is code is correct – this code will be falshed into the hardware/ Microcontroller/ ECU

---
 System Testing team
DBC file and the requirement
They will have Rahul;s python code. But they cant see the code.
Santhosh- They have to check if Rahusl code is correct/not?

---
Seat Belt ECU
Tester Node:
1. b- Send the “brake message=1”
Response= ‘seatbelt locked’
2. Send the accelerator message=0
Response= ‘seatbelt unlocked’
(DBC reference)
SEAT BELT ECU:
1. responds to brake message=1 ;
Lock the seat belt
2. Responds to an accelerator messag=0
Release the seatbelt
(Black Box)
CAN BUS

---
ENGINE ECU
Tester Node:
1. Send acceleration message
Response= ‘ Is speed increading by 10’
2. Send deacceleration message
Response= ‘ Is speed decreading by 10’
2. Send the brake message
Response= ‘Acceleration value=0’
(DBC reference)
Engine ECU:
1. Responds to acceleator message by
Increaing/decreasing speed
2. Responds to brake message by
bringing acceleration to ‘0’
(Black Box)
CAN BUS

---
Airbag ECU
Airbag ECU:
1. crash detected, engine is running,
 setabelt worn –
airbag will be released
2. crash detected, engine is not running/
Seatbelt not worn – sirbag is not ready
3. when no crash is detected- engine is running,
Seatbelt is worn- airbag is ready
Tester Node:
1. vehicle motion message – engine running/
crash detected, seatbelt msg,
Check
a.airbag released
b. airbag not ready
c. airbag is ready
CAN BUS

---
Trace
 Engine ECU
BUS
Display

---
ECU Block
Opens your ECU SIMX
 Engine ECU
Configure ECU
Simx
Save and
close
 the
file
Store the
python/capl/cpp script
linked with teh ECU

---
BUS
Config the bus- CAN/
VCAN/Ardino/STM
Socket CAN/Extended
CAN
BUS
SAve
Check if the bus config is available in ECU SIMX

---
Trace Window
Blank Screen
Choose the bus /
Candump any
Trace
Can Dump
Display all the
messages
Check if the bus config is available in ECU SIMX
PYQT 5
Challenge- Needs to integrate the qml file.

---
Display Window
Display
Trace
Set the ID
If accepted
During compiling it will check
and accept
Display the value
from the trace
In GUI